## Slide 1: SunSand IoT Monitor
[FILL IN: team member names + IDs]

## Slide 2: Project concept
Project idea #4 — IoT Environmental Monitor, extended end to end.
A bidirectional LoRa link + a WiFi-to-cloud dashboard on AWS.
Node reads sensors → safety rule → 433 MHz LoRa → gateway → WiFi/HTTP → AWS Flask → live web dashboard at iot.gabr.online:8080.
Demonstrates: 1-wire digital, ADC, GPIO, SPI+RF, half-duplex bidirectional radio, ESP32 WiFi + HTTP client, token-secured cloud API, FSM firmware with an EVAL/ALARM branch.

## Slide 3: Individual contributions
Member | Contribution
[FILL IN: name 1] | [e.g. Node A firmware + sensors + the EVAL/ALARM rule]
[FILL IN: name 2] | [e.g. gateway firmware + the bidirectional ACK]
[FILL IN: name 3] | [e.g. WiFi + cloud service + AWS deployment]
[FILL IN: name 4] | [e.g. dashboard + report + presentation]

## Slide 4
(Replace every [FILL IN] before presenting.)

## Slide 5: System block diagram
[Node A] --LoRa data--> [Gateway] --WiFi/HTTP--> [AWS EC2] --> browser DHT22 + photoresistor ESP32+LoRa Flask :8080 iot.gabr.online (EVAL/ALARM bonus) <--LoRa ACK-- + WiFi (token-gated)
LoRa hop is bidirectional (gateway ACKs every packet, node confirms).
WiFi is a non-fatal added stage — lose it and the link still LoRa-ACKs + prints to USB.
(Vector diagrams are in the report PDF.)

## Slide 6: Sensors used
Component | Interface | Role
ESP32-WROOM ×2 | — | MCU for node + gateway
LoRa Ra-01 (SX1278) ×2 | SPI | 433 MHz radio (both boards)
DHT22 ×1 | 1-wire digital | Temp + humidity, Node A
Photoresistor ×1 | Analog (ADC) | Light / day-night, Node A

## Slide 7: Circuit schematic (Node A)
+-----------+ GPIO4 DHT22 (temp/hum, 1-wire) Ra-01 ---| ESP32 | (SPI) | Node A | GPIO34 Photoresistor AO (ADC1) +-----------+
Ra-01 at 3.3 V (never 5 V) + 100 nF + ~17 cm antenna wire.
LoRa SPI: SCK 18 / MISO 19 / MOSI 23, NSS 5 / RST 27 / DIO0 26.
Gateway = same ESP32 + Ra-01, no sensors.

## Slide 8: State machine — Node A (bonus + ACK)
INIT -> READ -> EVAL --(hot|dark&humid)--> ALARM --. \ \ alarm=1 \--(safe)--> BUILD <--------------' | WAIT <- WAITACK <- SEND <--' (WAITACK listens ~600ms for ACK)
ALARM is a real extra state (overheat OR dark+humid).
WAITACK flips the radio to RX and confirms the gateway’s ACK,<seq>.

## Slide 9: State machine — Gateway (bridge)
INIT(LoRa+WiFi) -> LISTEN --(packet)--> PARSE -> EMIT -> LISTEN \--(5s)--> STATUS --^ EMIT = (1) LoRa ACK back (2) USB print (3) WiFi HTTP POST
ACK is sent before the POST — a slow hotspot can’t break the round-trip.
WiFi non-fatal: join fails → still ACK + USB, retry on heartbeat.

## Slide 10: Key code — the bonus safety rule
bool hot = (tempC >= TEMP_HOT_C); bool condensation = (night == 1 && humPct >= HUM_HIGH_PCT); state = (hot || condensation) ? S_ALARM : S_BUILD;

## Slide 11: Key code — bidirectional ACK
// gateway, on each received packet: sendAck(seq); // LoRa TX back to node (fast, first) Serial.println(out); // local debug cloudPost(out); // WiFi HTTP POST (may block; done last) // node, WAITACK: if (strncmp(rx,"ACK,",4)==0 && strtoul(rx+4,0,10)==sentSeq) ackOk=1;

## Slide 12: Cloud deployment
Flask cloud_app.py as a systemd service on AWS EC2, port 8080, own venv.
Co-tenant box runs an unrelated service on 80/443 — isolated by port, untouched.
One SG rule opens 8080; ingest gated by an X-Token secret.
Route 53 → iot.gabr.online. Token + WiFi creds gitignored (secrets.h).

## Slide 13: Additional features (bonus marks)
Bidirectional LoRa — gateway ACKs, node confirms; ACK before cloud POST.
WiFi cloud uplink — token-secured AWS dashboard reachable anywhere.
Environment-safety ALARM state — overheat / dark+humid; LDR participates.
Self-healing + graceful degradation — faults retry; WiFi loss ≠ outage.
Hardware-independent demo path — USE_LORA 0 → straight to USB.
Secrets hygiene — no credentials in committed code.

## Slide 14: Testing
Cloud: no/bad token → 403, good token → 204, packet shows in /data. Pass.
WiFi: 2.4 GHz scan found hotspot −30..−45 dBm; gateway joined (172.20.10.x), POST 204. Pass.
Dashboard --fake: renders, counters advance, day/night + alarm toggle. Pass.
[FILL IN: real-hardware RSSI at demo distance + sensor sanity ticks]

## Slide 15: Demo video
[EMBED OR LINK the recorded demo video here.]
Power gateway → # WiFi OK; power Node A → dashboard ONLINE + ACK ok on node serial; cover LDR → NIGHT; warm DHT22 → ENVIRONMENT ALARM banner; remove → clears.

## Slide 16: Conclusion
Met brief (idea #4); extended to a bidirectional link + cloud dashboard with an on-board safety state.
Clean FSM firmware, documented protocol, secrets hygiene, 6 bonus features.
Future: TLS on the uplink, gateway→node command path on the ACK channel, more nodes (protocol namespaces by node ID).
Thank you — questions?